## Slide 1: Seagliders as a multidisciplinary ocean observing platform
Rob Hall
School of Environmental Sciences
University of East Anglia
robert.hall@@uea.ac.uk
www.ueaglider.uea.ac.uk
With UEA colleagues Karen Heywood, Jan Kaiser, Gillian Damerell, Bastien Queste, Ben Webber, Adrian Matthews, Gareth Lee and Stephen Woodward
Notes: Introduction slide

## Slide 2: Seagliders : a new component of the ocean observing system
Ocean gliders weigh 50 kg in air, use buoyancy changes to descend/ascend
20-30 cm s-1 horizontal, 10-20 cm s-1 vertical speeds
Maximum profile depth 1000 m, minimum 50 m
At the surface, they transmit data back in real time via satellite & receive new piloting instructions
Surface every 15 minutes for shallow dives or 4-6 hours for 1000 m dives
Ideal for winter or rough weather
Work autonomously with set waypoints or in virtual mooring mode
Missions of up to ~ 6 months’ duration
Designed by UW, formerly licenced to iRobot, now to Kongsberg
Notes: Introduction slide

## Slide 3: Seaglider sensors
CTD – temperature, salinity and pressure
Dissolved oxygen O2 from Aanderaa optode
Chlorophyll and CDOM fluorescence (Wetlabs triplet puck)
Optical backscatter for particulate carbon (Wetlabs puck)
PAR solar radiation
Bioacoustic echo sounder for zooplankton biomasss
Dive-average current
Surface drift
Independent Argos tag on the glider antenna for emergency location

## Slide 4: UEA Seaglider Group Deployments to date:
UEA operates a fleet of 4 Seagliders
ueaglider.uea.ac.uk
Scotland, 2010, trials of 3 gliders, 90 dives, 5 glider-days
Vigo, 2010, 1 glider, 1611 dives, 113 glider-days
Ross Sea, 2010-2011, 1 UEA glider, 701 dives, 59 glider-days
North Sea, 2010, 1 glider, 181 dives, 5 glider-days
Indian Ocean, 2011-2012, 1 glider, 738 dives, 131 glider-days
Weddell Sea, 2012, 3 gliders, 795 dives, 104 glider-days
PAP, 2012-2013, 2 gliders, 4069 dives, 750 glider-days
North Sea, 2013, 1 glider, 2555 dives, 60 glider-days
Notes: Blue text slide with orange bullet points

## Slide 5
50 km section
17 sections June-August
1300 glider dives
UEA SeaGlider Deployment summer 2010 Iberian continental shelf and slope
CSIC Mytilus Transect
Salinity from Seaglider transect 4
(June 27th- July 3rd).

## Slide 6
No upwelling, limited productivity
Deep chlorophyll maximum at 30-45m depth
Isotherms are near horizontal
Oxygen depleted near surface
Large bloom event
Isotherms sloping indicating upwelling
Cooler near surface temperatures
Increase in oxygen
Net community production estimated using Seaglider dissolved oxygen measurements

## Slide 7
23 + 158 dives
CASE PhD studentship with Cefas
Mechanisms for oxygen depletion
UEA and Cefas Seaglider Deployment North Sea pilot study summer 2011
Metres above bottom
Metres above bottom
Metres above bottom
Temp
Chlor
Oxy

## Slide 8: New sensors on a Seaglider for krill dynamics
Imagenex echo sounder – for acoustic backscatter signal strength
120 kHz single beam echo sounder
Known acoustic characteristics
0.5 m bins, with range to 100 m
echo
sounder

## Slide 9: Osmosis gliders
Chart: 
| Sep-2012 | Oct | Nov | Dec | Jan-2013 | Feb | Mar | Apr | May | June | July | Aug | Sep
502 | 5 | 5 | 5 | 5
510 | 4 | 4 | 4
533 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3
566 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2
579 | 1 | 1 | 1 | 1
617 dives
519 dives
656 dives
655 dives
430 (590) dives
804 dives
Cond. sensor
Oxygen sensor

## Slide 10: Seaglider study of deepening and shoaling of mixed layer
Two gliders at the Porcupine Abyssal Plain time series site
Seasonal cycle in processes over one year
Multidisciplinary

## Slide 11: Brahan Project with Marine Scotland Science
October – December 2013
Water depth ~ 100 m
Tidal currents > 50 cm/s
>2500 dives
Deployment
Recovery

## Slide 12: Brahan Project with Marine Scotland Science
Temperature
Salinity
Potential Density
Oxygen Conc.
Deployment
Recovery

## Slide 13: Seaglider infrastructure
UEA now equipped to undertake refurbishments of Seagliders, including
testing of any faults/problems
battery replacement
replacement of all screws and sacrificial anodes
greasing of all gearings
formatting of flashcard
deep clean
compass check and possible calibration
reballasting for required ocean water density
Recalibration of sensors between deployments by manufacturers
Iridium transmissions using RUDIX

## Slide 14: Data processing and calibration
Real-time data are available straight away by ftp
Delayed mode data are calibrated and cleaned up
Flight model regressions to optimise data quality and calculate dive-average currents
Flags for good/bad/modified data
Thermal lag corrections for conductivity cell
Lag corrections for dissolved oxygen optode
Compare with CTD data for absolute calibrations
Calibrate dissolved oxygen, chlorophyll against samples
Vertical and horizontal gridding

## Slide 15: New Sensors for Gliders
New passive acoustic monitoring (PAM) sensor being integrated into Seaglider by Kongsberg
For marine mammal detection and monitoring of anthropogenic noise (2-50 Hz)
New pH and pCO2 sensors being integrated into Seaglider at UEA
For ocean acidification and marine carbon cycling
We are undertaking trials of both sensors in Mediterranean in June 2014 in conjunction with CMRE on RV Alliance
In future: microstructure sensors for turbulent mixing, ADCPs

## Slide 16: The Way Forward?
Ocean gliders can measure physics, chemistry and biology of the ocean simultaneously
Offer the opportunity to measure in remote areas and during rough weather, including near-surface values
Complement existing technologies such as moorings and HF radar
Real time data
Deployment from small boats or ships of opportunity